## Slide 1: PyRAT – Python Radar Tools …a short introduction… April 2016

## Slide 2: Part 1: PyRAT Usage

## Slide 3: Installation
Checkout from repository (into folder „pyrat“):
> git clone https://github.com/birgander2/PyRAT pyrat
Installation (also have a look at README.txt):
> cd pyrat
> ./setup.py install –user
After that, PyRat should be available for the respective user. The installation is located on the local python site-packages (usually: $HOME/.local/lib/…)
Only compiling (alternatively):
> cd pyrat
> ./setup.py build_ext –-inplace
In this case one has to work directly from the folder „pyrat“. This might be convenient when developing. Be careful with mixing both variants!

## Slide 4: Configuration
At startup, PyRat searches for a file „$HOME/.pyratrc“, containing the path to a dedicated directory for temporary files. Default is /tmp (usually a bad choice).
It is recommended to select a directory on a fast and large disc. This directory should be checked and cleaned up from time to time.

## Slide 5: Starting PyRAT
CLI Interface:
  From the command line:
  > ./pyrat.run –b [corresponds „from pyrat import *“, see later] or > ./pyrat.run --batch
or from the python prompt:
  >>> import pyrat [for scripts] or >>> from pyrat import * [simpler for working interactively, no prefix
  “pyrat” in front of every line]
GUI Interface (experimental, does not contain all the functionality):
  From the command line:
  > ./pyrat.run [rat filename]

## Slide 6: Embedded help system
  Help function (batch mode)
  >>> help() [list of available commands and modules] >>> help(function) [help for function] >>> help(module.function) [help for function in module]
  The requires docstrings in the programmed classes to be present. The quality might vary…
Overview of all existing data layers:
  >>> listlayer() or info()
/L1 Disc D float32 (2432, 6144)
/L2 Disc D float32 (4864, 12288)

## Slide 7: PyRat modules
PyRat contains (currently) the following modules:
  load: Import of data
  save: Export of data
  filter: Various image filtering and manipulation routines
  transform: Geometric transforms
  insar: Interferometric processing
  polsar: Polarimetric processing
  plugins: Various
  Content of a module:
  >>> help(module_name)

## Slide 8: The layer concept in PyRat
PyRat operates on abstract data layers, all processing is based on them
Each layer has a unique name (string, e.g. “/L7“)
Each layer contains data and metadata (stored in a temporary file)
New layer are generated by importing data sets (load module), or as result of a prior (intermediate) processing step (return value: name of layers)
Operations are always performed on one or several “active” layers
Processing results are automatically activated (and everything else deactivated)
Examples for commands for manipulating layers:
  >>> listlayer() Print list of all layers (aktiv = *)
  >>> activate(layer) Activate a layer
  >>> delete(layer) Delete a layer
  >>> var = getdata() Read data from layer into a numpy ndarray
  >>> addlayer(var) Write content of ndarray in a new layer
  >>> var = getmeta() Read der metadata (of active layer)
  >>> setmeta(meta) Change Metadata

## Slide 9: Example: Import of data:
From files or products (Examples):
>>> lay1 = load.rat(“abc.rat”)
>>> lay2 = load.fsar_slc(”/playground/14CROPXP/FL02/PS03/T01”)
Import typically reads data and metadata in new layers. lay1 and lay2 contain the names of these layers (not the layer themself!).
From memory:
Assumption: the data are already read somehow into a numpy-ndarray
>>> vx = addarray(ndarray)
>>> addmeta({´prf´: 1010.0}, ´lambda´: 0.056)

## Slide 10: Processing of data:
Applying a processing routine:
Each operation is applied to the active layer. Some routines require multiple input layers (e.g. image & DEM). If a keyword „layer“ is specified, it overrides the currently active layer(s). If needed, further options can be specified (otherwise default values will be used).
Examples:
>>> filter.boxcar() smoothing the active layer
>>> filter.lee(looks=3, layer=“/L3”) Lee filtering of layer “/L3“
>>> activate(“/L3”) Activating layer “/L3“
>>> filter.lee(looks=3) Lee filtering (of layer “/L3“)

## Slide 11: Saving results:
To binary rat file (example):
>>> activate(“/L7”)
>>> save.rat(filename=“abc.rat”)
To pixmap (example):
>>> save.pixmap(filename=“out.jpg”, order=[2,0,1], layer=“/L7”)
To memory / numpy ndarray:
>>> activate(“/L2”)
>>> var = getdata()

## Slide 12: Writing a pyrat script
Composition of a PyRAT script:
  #!/usr/bin/env python from pyrat import *
  pyrat_init()
PyRat Kommando 1
PyRat Kommando 2
Etwas Python
PyRat Kommando 3
Tricks:
pyrat_init(debug=True) Additional debugging output, no multithreading
pyrat_init(nthreads=2) Run with an alternative number of threads
Worker.blockprocess = False Switch off block processing (good for debugging)
Worker.blocksize = 512 Change default azimuth block size

## Slide 13: Complex Example: Entropie/Alpha Decomposition I
~> python
>>> from pyrat import *
INFO: Welcome to PyRAT V0.2
INFO: OS detected : linux2
INFO: Temporary directory: /playground/User/reigber/PyRAT_tmp
INFO: Pool with 8 workers initialised
>>> load.rat(filename="alling_k3l.rat")
INFO: RAT IMPORT {'is_activated': False, 'filename': 'alling_k3l.rat'}
WARNING: No meta data imported
INFO: Activating ['/L1']
>>> setmeta({'CH_pol': ['HH','VV','XX']})
>>> filter.lex2pauli()
INFO: LEXICOGRAPHIC TO PAULI CONVERSION {}
LEXICOGRAPHIC TO PAULI CONVERSION: [#############] 100%
INFO: Activating ['/L2']
>>> filter.vec2mat()
INFO: VECTOR -> MATRIX {}
VECTOR -> MATRIX : [############################] 100%
INFO: Activating ['/L3']
>>>> info()
/L1 Disc D complex64 (3, 4190, 1455)
/L2 Disc D complex64 (3, 4190, 1455)
/L3 * Disc D complex64 (3, 3, 4190, 1455)
“from import *” to avoid prefix „pyrat“ in each line of the script
Import of a *.rat (contains data, but no meta data!)
Explicit setting of meta dara (here: polarisartions)
Transformation into Pauli-basis
Generation of covariance matrices Kovarianzmatritzen
Print list of layers

## Slide 14: Komplexes Beispiel: Erzeugung einer Entropie/Alpha Dekomposition II
>>> filter.boxcar(win=[15,7])
INFO: BOXCAR FILTER {'phase': False, 'win': [15, 7]}
BOXCAR FILTER : [############################] 100%
>>> filter.eigen()
INFO: EIGEN DECOMPOSITION {}
EIGEN DECOMPOSITION: [###########################] 100%
INFO: Activating ['/L5', '/L6']
>>> lay = filter.entalpani()
INFO: H/a/A {}
H/a/A : [############################] 100%
INFO: Activating ['/L7', '/L8', '/L9', '/L10']
>>> save.rat(filename="out.rat", layer=lay[0])
INFO: RAT EXPORT {'filename': 'out.rat'}
>>> info()
/L1 Disc D complex64 (3, 4190, 1455)
/L2 Disc D complex64 (3, 4190, 1455)
/L3 Disc D complex64 (3, 3, 4190, 1455)
/L4 Disc D complex64 (3, 3, 4190, 1455)
/L5 Disc D float32 (3, 4190, 1455)
/L6 Disc D complex64 (3, 3, 4190, 1455)
/L7 * Disc D float32 (4190, 1455)
/L8 * Disc D float32 (4190, 1455)
/L9 * Disc D float32 (4190, 1455)
/L10 * Disc D float32 (4190, 1455)
Apply boxcar-filtering with the option win=[15,7]
Eigen decomposition of the result
generates 2 new layers: Eigenvalues and vectors!
Processing of Alphamax, Alphamean, Entropy and Anisotropie
Export of layer „/L7“ into the file „out.rat“
Again a list of existing layers. One should have deleted some intermediate results (with the command „delete“). When existing python, an automatic cleanup is performed.

## Slide 15: Easter Eggs:
The GUI can be launched from a pyrat-Script (or interactively) :
>>> show() bzw. gui()
The active layer will be shown in the GUI (one can scroll and zoom in and out…)
Saving and Restoring of the entire layer structure and of 3 local variables
>>> freeze(“filename.hd5“, var1, var2, var3)
>>> x1, x2, x3 = defreeze(“filename.hd5“)
Complexe layer structures:
When a nested layer list is used (active, or via keyword), data will be returned in exactly this structure (nested list of ndarrays).

## Slide 16: Part 2: Programming PyRAT

## Slide 17
PyRAT - Pyton Radar Analysis Tool
Layer based data object (HDF5 / RAM)
CLI Interface (scriptable)
GUI Interface (PyQt / PySide)
Worker (Import / Export / Filter)
Plugin
Motivation:
Flexible framework for SAR postprocessing
Suitable for airborne- and satellite data
Collection of state-of-the-art tools
Software design goals:
Implementation in Python
Disc based processing in HDF5-containers, including metadata and tracks / orbits
Automatic block processing (multithreaded)
Abstract worker classes – easy to implement without much knowledge of the framework
Optional: Qt-based GUI for simple tasks and a a data viewer
Simple extensions via plugin infrastructure

## Slide 18
LayerData: The central data object
Content of a layer:
Data (as ndarray)
Metadata (as dictionary)
Channel metadata
Properties (intern)
3 Variants:
Disc layer (HDF5): Does not need RAM, possibly a bit slow
Memory layer: Faster (depending on available cache)
Virtual layer: Mapping of existing data sets, avoids copies
Possibilities:
Reading / Writing of data (possibly in groups, in parts)
Reading / Writing of meta data (possibly in groups)
Activating, adding, deleting and listing of layers
/L1
/L2
/L3
/L3/D1
/L3/D2
/L3/D3
/L3/D4
/L3/P
+ metadata
Pseudo-Verzeichnisstruktur:

## Slide 19
FilterWorker: Basis Class Data Processing
Capabilities:
Reading from a layer
Testing if data have suitable format (shape, dtype) and if all required meta data is available
Processing of data (and meta data)
Block processing (can be activated and deactivated)
Using the PyRAT multiprocessing pool (can be activated and deactivated)
Writing into a new layer
Show its docstring
Goals:
Vast simplification of the implementation of data processing routines
+ Further Workers: Import, Export, Layer, …, ???

## Slide 20
Programming a new Filter
TODO:
Implementation of a Class according to example (see: filter/Template.py)
  Description of the parameters (dict as class variable, see example)
  Write the actual functionality, in the method “filter”: This is practically pure processing code without much PyRAT stuff required. The data are delivered in a variable “array”, meta data as “kwargs[‘meta’]”.
  Add comfort functions (two lines, see example)
  Write documentation into the docstring!!!
Extend the __init__.py file in the respective subdirectory by the needed import line (or put your code in the plugins directory )
Warning: For debugging, don’t use blockprocessing (self.blockprocessing=False), or at least only one thread (self.nthreads=1). Otherwise, you’ll have troubles with pdb….
Import and ExportWorker are slightly different, but very similar.
Totally free modules must be derived directly from pyrat.Worker, but then a bit more “hand work” is necessary.

## Slide 21
Programming a new Filter
Generally:
Since programming documentation is minimal, and development of PyRAT is ongoing (and changes to the API are likely):
Feel free to ask the developers directly !
It’s quite easy to add something!